## Slide 1: DEPARTMENT OF INFORMATION TECHNOLOGY
Project Name: ENVIRONMENTAL MONITORING
Team Name: Proj_224786_Team 5
Team Members:
JEEVAN SIVA SANKAR A (113321205021) SELVA KUMARAN T (113321205046)
SRIDHAR B (113321205051)
SABAREES S (113321205301)

## Slide 2: Problem Statement:
In today’s rapidly changing world,there is a growing concern about the state of environment.Climate change,pollution and natural disasters are posing significant threats to our planet and the well-being of it’s inhabitants.To adress these challenges,there is a processing need for an advanced Environment Monitoring System(EMS)that can provide real-time data on key environmental parameters.This system should be capable of monitoring and reporting on factors such as air quality,temperature,humidity,water quality and more in various location and ecosystems.

## Slide 3: Objectives:
Assessment Of Environmental Quality:
To evaluate the overall health and quality of natural ecosystems including air,water,soil and biodiversity.
Detection Of Pollution:
To identify and quantify the presence of pollutants,contaminants and hazardous subsatnces in the environment.
Early Warning Of Environmental Risks:
To provide timely warnings of potential environmental disasters,such as floods,wildfires,or chemical spills.
Compliance Monitoring:
To ensure that industrial and human activities are in compilance
with environmental laws and regulations.

## Slide 4: INTEGRATION APPROACH:
List all the components, systems, or elements that need to be integrated. This can include hardware, software, processes, data sources, and external systems.
Assess Compatibility
Select Integration Technologies
Design Integration Architecture
Data Mapping and Transformation
Develop Integration Code or Configurations
Testing and Validation
Security and Logging
User Training and Documentation
Change Management
Communication and Reporting

## Slide 5
PYTHON CODE
# SPDX-FileCopyrightText: 2018 Brent Rubell for Adafruit Industries
# SPDX-License-Identifier: MIT
# Adafruit IO Environmental Monitor for Feather or Raspberry Pi –
# an internet-enabled environmental monitor
# Import standard python modules import time
# import Adafruit Blinka import board import busio
# import CircuitPython sensor libraries
import adafruit_sgp30
import adafruit_veml6070 from adafruit_bme280 import basic as adafruit_bme280
# import Adafruit IO REST client from Adafruit_IO import Client, Feed, RequestError # loop timeout, in seconds. LOOP_DELAY = 10

## Slide 6
try: # if we already have the feeds, assign them.
tvoc_feed = aio.feeds('tvoc') eCO2_feed = aio.feeds('eco2')
uv_feed = aio.feeds('uv')
temperature_feed = aio.feeds('temperature') humidity_feed = aio.feeds('humidity')
pressure_feed = aio.feeds('pressure')
altitude_feed = aio.feeds('altitude') except RequestError: # if we don't, create and assign them. tvoc_feed = aio.create_feed(Feed(name='tvoc')) eCO2_feed = aio.create_feed(Feed(name='eco2'))
uv_feed = aio.create_feed(Feed(name='uv')) temperature_feed = aio.create_feed(Feed(name='temperature')) humidity_feed = aio.create_feed(Feed(name='humidity')) pressure_feed = aio.create_feed(Feed(name='pressure')) altitude_feed = aio.create_feed(Feed(name='altitude'))

## Slide 7
# Create busio I2C i2c = busio.I2C(board.SCL, board.SDA)
# Create VEML6070 object. uv = adafruit_veml6070.VEML6070(i2c)
# Create BME280 object. bme280 = adafruit_bme280.Adafruit_BME280_I2C(i2c) bme280.sea_level_pressure = 1013.25
# Create SGP30 object using I2C. sgp30 = adafruit_sgp30.Adafruit_SGP30(i2c) sgp30.iaq_init() sgp30.set_iaq_baseline(0x8973, 0x8aae)
# Sample VEML6070 def sample_VEML():
for _ in range(10):
uv_raw = uv.uv_raw return uv_raw
while True:
print('Reading sensors...')
# Read SGP30.
eCO2_data = sgp30.eCO2
tvoc_data = sgp30.TVOC

## Slide 8
uv_data = sample_VEML()
# Read BME280. temp_data = bme280.temperature
# convert temperature (C->F)
temp_data = int(temp_data) * 1.8 + 32
humid_data = bme280.humidity pressure_data = bme280.pressure
alt_data = bme280.altitude
print('sending data to adafruit io...')
# Send SGP30 Data to Adafruit IO. print('eCO2:', eCO2_data) aio.send(eCO2_feed.key, eCO2_data)
print('tvoc:', tvoc_data)
aio.send(tvoc_feed.key, tvoc_data) time.sleep(2)
# Send VEML6070 Data to Adafruit IO.
print('UV Level: ', uv_data)
aio.send(uv_feed.key, uv_data)
time.sleep(2)

## Slide 9
print('Temperature: %0.1f C' % temp_data)
aio.send(temperature_feed.key, temp_data)
print("Humidity: %0.1f %%" % humid_data)
aio.send(humidity_feed.key, int(humid_data))
time.sleep(2)
print("Pressure: %0.1f hPa" % pressure_data)
aio.send(pressure_feed.key, int(pressure_data))
print("Altitude = %0.2f meters" % alt_data)
aio.send(altitude_feed.key, int(alt_data))
# avoid timeout from adafruit io time.sleep(LOOP_DELAY * 60)

## Slide 10
CONCLUSION
In conclusion, environmental monitoring plays a crucial role in safeguarding our planet and ensuring the well-being of both current and future generations. It serves as a vital tool for tracking the state of our environment, identifying emerging issues, and guiding decision-makers toward more sustainable practices. The information collected through various monitoring techniques, such as air and water quality assessments, wildlife tracking, and climate change observations, helps us understand the impact of human activities on the natural world.
Environmental monitoring empowers us to take proactive measures to mitigate the adverse effects of pollution, habitat destruction, and climate change. It provides us with the data needed to develop effective policies, make informed choices, and hold responsible parties accountable for their actions. Moreover, it allows us to assess the success of conservation efforts and adaptation strategies.

## Slide 11: THANK YOU